## Slide 1: Model-BASED SOFTWARE DEVELOPMENT LIFECYCLE
TEC-ED & TEC-SW Final Presentation Days - December 9th 2015
Joan Clua, Patricia López Martínez, Dominique Torette, Jorge Garrido

## Slide 2: Project Overview
MBSDL
Model-Based Methodology Review
  Define a methodology covering the entire SW lifecycle
  Work on ECSS to accommodate MSDL-based projects (deliverables, phases, reviews…)
  TASTE Extension
  Take the TASTE toolset as a baseline for tool selection to implement defined methodology.
  Explore areas where lifecycle is not deeply covered by the toolset (requirements, V&V…)
  Add tools and integrate them in the toolset
  Proof of Concept in a Mission
  Define specific mission (Flight Formation based).
  Implement the mission using the toolset produced in the project.
  Exercise point of view of SW developers, system engineers and reviewers

## Slide 3: Consortium
Barcelona
Delft
Liège
Madrid
Santander
MBSDL
  Project Coordination
Indra
  Model-Based Methodology Review
Universidad de Cantabria (UC)
Universidad Politécnica de Madrid (UPM)
Spacebel
  TASTE Extension
Indra
UC
UPM
  Proof of Concept in a Mission
TU Delf (Mission Definition)
Spacebel (Mission Implementation)

## Slide 4: TOC
MBSDL
01 Model Based Methodology (P. López, UC)
02 Timing Analysis in TASTE (J. Garrido, UPM)
03 Mission Proof of concept (D. Torette, Spacebel)
04 Conclusions

## Slide 5
01 Model Based Methodology (P. López, UC)
02 Timing Analysis in TASTE (J. Garrido, UPM)
03 Mission Proof of concept (D. Torette, Spacebel)
04 Conclusions

## Slide 6: MBSDL – Starting point
01 Model Based Methodology
Notes: The software development lifecycle that was considered the most suitable for the proposal is based on a typical V-model.
In fact, The ASSERT/TASTE approach that represented the starting point of the project have already addressed the lifecycle phases related with design and implementation. They were already supported by the TASTE environment and the purpose of the project was to improve and complemente them with the rest of phases of the lifecycle.
Finally, we have focused mainly on the specification phase.

## Slide 7: MBSDL – Early model-based analysis
01 Model Based Methodology
Notes: process leads to a lifecycle that does not follow strictly a V-model. When applying a traditional V-model approach, the V&V activities do not start until the code is available.
early V&V can be applied on the models generated as result of each phase of the development

## Slide 8: MBSDL DEfinition
Driven by specification of the problem
Specification Model
Traceability
Driven by architecture
of the solution
Design Model
(AADL)
Build the
System
Architectural Design
Detailed Design
Implementation
Requirements Engineering
Integration Testing
System
Testing
Test the
System
Unit Testing
An architecture-centric and specification-centric lifecycle
(RDAL)
01 Model Based Methodology
Notes: TASTE adopts an architecture-centric model approach for the design and implementation phases, based on AADL. As shown in the figure below, there is a unique design model, formulated on AADL, which supports directly the purely architectural aspects, such as modularization, interfaces, etc.
Other aspects, such as functional behaviour, real-time behaviour, etc. are supported by specific models that are referenced from the design model or generated from annotations on it.
A similar approach is going to be followed for supporting the requirements specification and V&V phases of the lifecycle. Thus, our proposal is that they will also rely on a single model, the Specification model, which will support directly or by reference all the information generated or managed on these phases.
For formulating such a model, a requirements modelling language such as RDAL or GRL, is the most suitable option. These languages provide direct support for modelling requirements, but also provide with capacity to associate requirements with other kind of models, such as use cases, functional specifications, tests descriptions, scenarios, etc. used to analyse, document, and understand the requirements. So, the figure below shows how the proposed lifecycle is supported by these two backbone models (design and specification models) and how they must provide backward and forward traceability in order to validate the design against the specification.
Considering that the entire development process is supported by a single model, or more exactly by two complementary models, the purpose of each phase in the lifecycle is the generation of different perspectives or views of the model, which contain (or add to the model) the information that is characteristic (or is the result) of the specific phase or task. In the next section each phase of the development is explained in detail, showing the tasks that are carried out on each phase and the views of the models that they generate.
Este concepto de la verificación temprana se ha tratado de aplicar en el proyecto MBSDL.
En él se partía de un modelo de ciclo de vida centrado en al arquitectura. Esta es una estrategia propuesta por el SEI que se basa en utilizar el modelo de arquitectura como el modelo central del proceso de desarrollo, en el que además de la arquitectura sirva para dar soporte a todo el conjunto de propiedades extrafuncionales a las que se les puede ir aplicando los análisis tempranos
Los aspectos propiamente arquitecturales como flujo de control, modularización e interfaces son soportados por el propio modelo AADL, mientras que otros aspectos (funcionalidad, comportamiento temporal, gestión de memoria, etc.) utilizan modelos específicos (diagramas de estados, modelos de comportamiento temporal, etc.) que por extensión o por referencia están incorporados al modelo AADL. Este proceso de diseño es lo que en la figura 10.6 se engloba dentro del “Design Model”.
El proyecto MBSDL, en el que participa el grupo ISTR, tenía como punto de partida el proceso de diseño definido en el proyecto ASSERT, y su objetivo era mejorar la aplicación del resto de pilares de la estrategia del SEI, esto es, mejorar la trazabilidad entre las fases de diseño y de especificación y verificación. Para ello, se consideró conveniente organizar también los modelo de especificación y de verificación en base a un modelo genérico que sirva de columna vertebral común a toda la información gestionada desde ellos.
l resultado es por tanto, un modelo de ciclo de vida del software sustentado por dos modelos principales, cómo se observa en la :
  El modelo de requisitos, que da soporte (de manera directa o por referencia) a toda la información asociada a las fases de requisitos y de verificación y validación.
  El modelo de diseño, que sustenta las fases de diseño e implementación.
Cómo es lógico, estos dos modelos deben presentar trazabilidad bidireccional entre sí, pues un aspecto vital del proceso de desarrollo consiste en validar la
implementación respecto a su especificación.
Considerando que el proceso completo de desarrollo es soportado por estos dos modelos complementarios, el objetivo de cada una de las fases de desarrollo es la de generar las diferentes vistas del modelo, que contienen (o añaden al modelo central) la información resultado de dicha fase de desarrollo.

## Slide 9: RDAL Language
RDAL: Requirements Definition and Analysis Annex
  AADL Annex but independent from it
  In process of standarization
  Traceability to design elements, functional models, reactive models, V&V Actitivites, etc.
01 Model Based Methodology
Notes: RDAL provides capacity to model requirements, with their typical attributes as priority, interested stakeholders, rationale, id, etc. It also allows to define requirements hierarchy and traceability.
But also provide with capacity to associate requirements with other kind of models, such as Use case maps or SDL diagrams to define the functional behaviour specfiication, tests descriptions, scenarios, etc. used to analyse, document, and understand the requirements.
It also provides capacity to trace the requirements to elements of the preliminary design, which will be later refined in the design phase, and to veriification activities, which can be defined also according to standard specifications as TTCN-3.
Desde un punto de vista más concreto, los lenguajes que se utilizaron en el proyecto MBSDL para impelmentar los modelos arquitecturales y de requisitos fueron AADL Y RDAL.
RDAL define un metamodelo que por un lado da soporte a la especificación de los requisitos propiamente dichos, con todas sus características típicas como identificador, descripción, prioridad, versión, stakeholders interesados, etc.; pero además como representa la figura 1.5, proporciona mecanismos que permiten incorporar a la especificación de requisitos:
• trazabilidad entre requisitos,
• trazabilidad entre requisitos y elementos del diseño,
• trazabilidad entre requisitos y sus correspondientes actividades de verificación y validación,
• trazabilidad entre requisitos y otros elementos de modelado, como casos de uso, especificaciones funcionales, etc. que faciliten la propia tarea de definición de requisitos.

## Slide 10: SOFTWARE REQUIREMENTS SPECIFICATION IN MBSDL
Context Modelling (AADL)
Context View
Requirements View
High-level Goals/Req Definition
(RDAL)
Functional Modelling
(UCM)
Logical Architectural Modelling
(AADL)
Functional View
Interface View
Behavioural Modelling
(SDL)
Behavioural View
Goals/Req Refinement
(RDAL)
Data Modelling
(ASN.1 and AADL)
Data View
Validation Tests Identification and Formulation
(RDAL)
V&V View
01 Model Based Methodology

## Slide 11: TOOL Selection
MBSDL Phase | Tools
Requirements Specification | RDALTE (RDAL Tool) jUCM (Use Case Maps Tool) + OpenGeode (SDL Tool) AADL + ASN.1
Software Architectural Design | AADL + ASN.1 OpenGeode (SDL) MAST/Cheedar (Schedulability Analysis)
Software Components Design | AADL + ASN.1 OpenGeode + Simulink/SCADE/RTDS MAST/Cheedar
Implementation | TASTE Code Generators
Software Testing | Rapita AADL + MAST/Cheedar MSC Test Tracer (TASTE)
01 Model Based Methodology
Notes: Several tools can be used to model or analysis the different aspects involved in the development of a space application. We address a survey of tools, analizing their main advantages and drawbacks and the final selection was the one presented here.
We use RDAL as the backbone of the requirement specification phase, improved with the usage of UCM maps and SDL diagrams for the logibal model of hte applicaton
We use AADL and ASN.1 for the design phase, and thanks to AADL extensions we can include information that allow us to apply schedulability analysis based on tools such as MAST and Cheedar.
Simulink can be used at the desing level to define the specific behaviour of some AADL modules, whose code can be automatically generated from the model.
We have integrated also

## Slide 12
01 Model Based Methodology (P. López, UC)
02 Timing Analysis in TASTE (J. Garrido, UPM)
03 Mission Proof of concept (D. Torette, Spacebel)
04 Conclusions

## Slide 13: WORK OVERVIEW
Objective: provide a working integration of Rapitime
  Structural analysis
  Execution time analysis
UPM and Rapitime Systems collaboration
  Rapita Systems:
    Provision of tools
    Initial integration version
  UPM:
    Providing previous integration as starting point
    Support on TASTE internals
    Versions iteration with Rapita
    Validation of final integration
02 Timing analysis in TASTE

## Slide 14: Rapitime overview
Based on:
Structural analysis of the code (compiler and user aided)
Automated instrumentation points
Execution traces
Provides:
Automated timing analysis framework
Execution paths analysis
Timing behavior of the system (including WCET estimation)
Graphical and textual results
Other analysis offered in Rapita Verification Suite (RVS)
On-target timing analysis tool
Rapitime process
02 Timing analysis in TASTE

## Slide 15: Integration overview
Integration based on previous version by UPM
Aimed to follow TASTE methodology:
  Command-line based process
  Python and bash scripts
  Text-files results
  Automated system analysis based on AADL and Ocarina generated files
  Integration within assert-builder-ocarina.py with new parameter –instrument
  Two-steps integration:
  First build generates system as usual
  Second build generates instrumented system at an auxiliary directory
02 Timing analysis in TASTE

## Slide 16: Integration results
Automated timing analysis for TASTE projects
Textual and graphical results
  Stored in a SQL database
  Textual output customizable
== project.vt_ground_result_wrappers.artificial_result.rvd
vt_ground_result_wrappers.artificial_result: 4077 cycles
== project.vt_myfunction_pulse_wrappers.artificial_pulse.rvd
vt_myfunction_pulse_wrappers.artificial_pulse: 73745 cycles
== project.vt_myfunction_start_processing_wrappers.artificial_start_processing
vt_myfunction_start_processing_wrappers.artificial_start_processing: 2328 cycles
02 Timing analysis in TASTE

## Slide 17: Integration results
02 Timing analysis in TASTE

## Slide 18: Integration results
TASTE overhead
TASTE overhead
User code
Subcalls
02 Timing analysis in TASTE

## Slide 19: Integration results
02 Timing analysis in TASTE

## Slide 20: Integration results
02 Timing analysis in TASTE

## Slide 21: Integration results
02 Timing analysis in TASTE

## Slide 22
01 Model Based Methodology (P. López, UC)
02 Timing Analysis in TASTE (J. Garrido, UPM)
03 Mission Proof of concept (D. Torette, Spacebel)
04 Conclusions

## Slide 23: Use case
03 Mission Proof of concept
Software Requirement Specification for a Formation Flying Mission
  GNC FF Algorithms
  FF Operational modes
  Distribution of the responsibilities across the formation
  Routing of PUS TM/TC
  Ground and Inter Satellites Link communication interfaces
Top inputs : High Level Specifications from TUDelft
  Introduction to AOCS/GNC functionalities of FF Satellites
  Mission Requirement Document
  System Requirement Document
  Operational Requirement Document
Additional inputs : In-house ongoing PROBA-3 FF project feedbacks

## Slide 24: Outputs
Models
  Specification and Documentation Generation
    Use Case Maps : URN/UCM
    RDAL : RDAL
  Design and Code Generation
    TASTE (Interface, Deployment) : AADL
    TASTE (Data model) : ASN.1
    TASTE/OpenGeode (Behavior, modes) : SDL
  Traceability links
  ECSS-like documentation (Fully generated from models - template based)
  SSS
  SRS

## Slide 25: User Requirements Notation (URN)
03 Mission Proof of concept
User Requirements Notation (URN) is intended for
  Elicitation and specification of requirements.
    Discover and specify requirements for a proposed system
  Analysis and validation of requirements.
    Analyze such requirements for correctness and completeness
      Execution of Scenarios and branches coverage
    Simple formal language for Behaviors and Scenario expected results definition
  Impact analysis of Implementation Trade-Off.
    Explore impacts of alternative responsibilities assignments.
  Graphical Representation
    Visually communicate design choices

## Slide 26: Use Case Maps (UCM)
Use Case Maps (UCM)
  graphically describes the functional requirements of a software system,
  precisely describe processes (alt. view to Message Sequence Chart),
  represents control flows and distributes responsibilities to actors, by superimposition of scenario paths on a structure of components.
Use Case Ma p fairly addresses
  operational requirements,
  functional requirements,
  architectural trade-offs.
At later stages, UCM may be further refined into:
  MSCs or UML sequence diagrams,
  SDL state machines or UML state chart diagrams.
  No new concepts, but same concepts introduced earlier in the development cycle.
03 Mission Proof of concept

## Slide 27: jUCMNav
UCM Tool
Free Eclipse-based plug-in/editor
  Now in version 6.0, August 2014
  Since May 2006
Dedicated Perspective, Graphical editor with palette
Eclipse Navigator, Outline view and Preferences
EMF metamodel
  Allows model to model and model to text transformations
Export to graphical representations (.jpg, .dot, .png)
Export to Message Sequence Charts (.jucmscenarios)
  Included Message Sequence Charts viewer
Allows the early definition, execution and verification of Scenarios
Allows graphical animation of Scenarios
Cross platform (Linux, Windows 7, Mac OS X)
03 Mission Proof of concept

## Slide 28: JUCMNaV: Perspective
03 Mission Proof of concept

## Slide 29: JUCMNaV: Palette
Structure of components
  Team, Object, Process, Agent, Actor.
Scenario paths
  Start Point : Scenarios initial conditions
  End Point : Scenarios completion conditions
    This is the place to allocate/verify requirements
    Textual description, but also formal expression to be verified on scenario completion. Boolean expression based on variables updated by Responsibilities.
  Or Fork : Execution path Or Fork (logical conditions)
  And Fork : Execution path And Fork (logical conditions)
  Or Join : Execution path Or Join
  And Join : Execution path And Join
  Responsibility: Pseudo-code fragment
  Stubs : Hierarchical decomposition, refer another UCM
03 Mission Proof of concept

## Slide 30: JUCMNAV: CODE/CONDITION EDITOR
03 Mission Proof of concept
Editor for
Responsibility code
Requirement condition
Variables list
Variables creation
Syntax Verification

## Slide 31: JUCMNAV: SCENARIO EXECUTION
03 Mission Proof of concept
Scenario:
Start points
Initializations
End points
Inclusions
Scenario Group:
Run all
Coverage
Unsatisfied Conditions reported as errors in problems panel

## Slide 32: JUCMNAV: Message sequence chart Export
03 Mission Proof of concept
Once Executed scenarios can be exported and viewed as MSC

## Slide 33: GENDOC: MODEL BASED SSS Generation
03 Mission Proof of concept
Template based Model2Txt transformation
EMF
Embedded Acceleo in .odt or .docx templates
Support for tables and figures
Test coverage and requirements traceability's

## Slide 34: RDAL METAMODEL: System OVERVIEW
03 Mission Proof of concept
Identification of
the System and
its Environment.
Identification of Data Interface.
Concept of
Monitored Variables
Controlled Variables
but only at top level.
Similar to Simulink Block inputs/outputs.

## Slide 35: RDAL METAMODEL: Requirement
03 Mission Proof of concept
Organized in Packages
Complex structure, oversized for mid-size project
Reference to external models (traceability) through EObject
Natural language
Formal languages: BLESS, Lute, OCL but no provers support

## Slide 36: RDAL TOOLING: RDALTE
03 Mission Proof of concept
EMF meta-model
EMF Sample Reflective Model Editor
Live validation
Export to textual representation
RDAL Graphical Representation V2 not yet implemented by RDALTE

## Slide 37: GENDOC: MODEL BASED SRS Generation
03 Mission Proof of concept
Same M2T tooling as for jUCMnav
No graphical representation

## Slide 38: TASTE: AADL and ASN.1 OPEN-SOURCE EDITOR
03 Mission Proof of concept
Chaser GNC Simulink
Chaser System modes SDL
Model2Code
C, Ada, GUI, VHDL

## Slide 39: OpenGEODE: SDL OPEN-SOURCE EDITOR
03 Mission Proof of concept
SDL Events:
TC, FDIR,…
SDL variables
SDL Actions:
On/Off, counters
SDL States: System modes
ASN.1
Data Model
Equivalent
FSM
Model2Code
Ada and LLVM
Static Analysis

## Slide 40
01 Model Based Methodology (P. López, UC)
02 Timing Analysis in TASTE (J. Garrido, UPM)
03 Mission Proof of concept (D. Torette, Spacebel)
04 Conclusions

## Slide 41: Conclusions
04 Conclusions
Software Requirements Specification has been integrated into a Model Based Software Development Lifecycle
Use Case Maps and rdal language tools have been integrated in TASTE
The methodology and the tools have been evaluated on a realistic mission
Rapitime has been integrated in TASTE
Software Requirements can be adequately modelled using rdal and UCM, providing a bridge with system architects
TASTE is an excellent platform to add new functionality

## Slide 42
Joan Clua jclua@indra.es
Joan Ametller
Marc García
Laura Perea
Marcos Venteo
Patricia López Martínez lopezpa@unican.es
Michael González Harbour
Dominique Torette Dominique.Torette@spacebel.be
Paul Parisis
Philippe Créten
Jorge Garrido jgarrido@dit.upm.es
Juan Antonio de la Puente
Jian Guo J.Guo@tudelft.nl
Model-BASED SOFTWARE DEVELOPMENT LIFECYCLE
TEC-ED & TEC-SW Final Presentation Days
December 9th 2015
Thank you very much for your attention