## Slide 1: 24/11/21
GSTP Armony

## Slide 2
Background & Justification
OBSW developed for ARM processors are more and more present in spacecraft OBC and payloads
SPACEBEL strongly believes in the interest of full numerical solution of the validation of embedded software
ARM emulators COTS do not match the specific needs and constraints of space application validation
  Precise timing evaluation
  Non-invasive debugging capabilities
  Integration within existing simulation infrastructure
  Scaling

## Slide 3
Goal of the Activity
Design a generic & modular ARM processor emulator
  Cortex-A9 Zynq-70xx main target @650MHz
  Simulation Model packages, SMP2 compliant & SMP compatible
  With easy extension to build SoC virtual platform
Develop a Xilinx Zynq-70x0 ARM A9 emulator
  With real-time execution of an unaltered OBSW
  With debug and introspection means for OBSW VS&QA

## Slide 4
Objectives
Actual dates matched the schedule, except for the CDR
  Needed to change the reference OBSW for final acceptation
    Instruction set upgrade (T16/T32/SIMD)
    Additional peripheral and I/O extension
    Additional feature (MMU)
 | Initial | Actual
KO | 09/2021 | -
PDR | 01/2021 | 12/2020
DDR | 07/2021 | 06/2021
CDR | 02/2021 | 11/2022

## Slide 5
Description of the Solution
Internal JIT engine of the core
  External unmodified TCC compiler included as library (LGPL)
  Deterministically generates Execution Block based on instructions lines read from memory, and currently active optimisations
  Just-In-Time compilation is very fast because of the under-usage host hardware, and smart arrangement of blocks
  Block discovery at runtime, in parallel of the OBSW execution
Time correlation module
  Synchronize OBSW timeline with the extension/simulator ones down to the nanosecond
Environment Extension IF
  Easy integration at the level of memory bus access, coprocessor, interrupt signal

## Slide 6
Work Logic
Emulator developed iteratively
  Quickly stabilize a first version
    To prove target performance
    To define a modular architecture that will allow parallel development and easy evolution
  Validate first versions if JIT engine with a reference ARM emulator
  Each iteration support complete cycle: design, implementation & verification, to provide fully validated added-value
Additional studies were led in parallel to support design & implementation choices

## Slide 7
How it has been validated
Armony comes as two products
  Standalone: only ARM-A9 emulator, limited extension
    Validation performed by the point-of-view of the OBSW
    All registers & context dumped during the run of reference softwares, thanks to the tracing capabilities of the emulator
    Comparison with the same results from QEMU
  Zynq virtual platform
    Several level of reference software: bare-metal, FreeRTOS system, XtratuM, XNG
    Peripheral unit-testing
    OBSW-profile reference image made by CNES

## Slide 8
Issues
Genericity of ARM
  Not only the emulator architecture must be modular, but the elaboration of cores, instruction set, memory, coprocessor and peripheral must allow numerous different configurations
Challenging to integrate black box OBSW
  We created a code discovery algorithm that is capable to detect instruction and compile executable block from any kind of image format (no symbol required)
  No source makes bugfix very difficult
  Astonishing to find out that Thumb is still used
  Also to find out that old/banned instructions are still used

## Slide 9
Results
TSP demonstrator executed at 411 MIPS
  Centos 8.2/Intel® i9-12900K Core @ 3.20GHz
Compilation time by JIT engine of the OBSW
  ~70.000 instructions
  20 seconds, distributed on the whole execution of the OBSW

## Slide 10
Way Forward
Initial goals are fulfilled
We are now integrating the emulator in an operational TOMS
What’s Next
  Upgrade to ECSS SMP standard: done 05/2023
  Extend the target ARM CPU: R5, R4F and R52
  Extend the Armony library of standard and custom IP
  Improve performance
    Reduce critical path in kernel feature
    Embed kernel services closer to JIT engine
    Parallelisation of multi-core