## Slide 1
ESA Contract No. 4000136329/21/NL/MG
EVACPRO
Chemical Modelling of Reactions and Processes in Propellant Systems
Empresarios Agrupados Internacional (EAI)
https://www.ecosimpro.com/products/espss/
Final Presentation 2023 / 11 / 29

## Slide 2: Agenda
 | Topic | 
1 | Introduction | 5’
2 | Project Organization | 10’
3 | Review of modelling approaches | 15’
4 | Review of ESPSS components | 15’
5 | Review of validation | 15’
6 | Q&A | 20’
7 | Closeout/AoB | 10’

## Slide 3: Introduction

## Slide 4: Introduction
Project goal: The objective is to improve ESPSS capabilities applied to transient simulations of complete chemical propulsion systems using novel propellants. Agreement of 10% during operation sequence.
  Branch 1: LOX/ CH4. M10 Upper Stage
    Task1: Model identification
      Turbo-machinery thermal, mechanical and fluid dynamic transient models.
      Reduced-order finite rate chemistry models for LOX/CH4.
      Pyrolysis and coking phenomena within cooling jackets.
      Heat and mass transfer in novel injectors for LOX/CH4.
    Task2: Implementation
    Task3: Validation
  Branch 2: Monopropellant case. RACS – VEGA C
    Task1: Model identification
      Instabilities modelling in the catalysts of monopropellant thrusters.
      Reduced-order finite rate chemistry models for H2O2 and other green propellants.
      Chemistry models for H2O2 and other green propellants.
      Injectors modelling for monopropellants.
    Task2: Implementation
    Task3: Validation

## Slide 5: Project organization

## Slide 6: Project Team Organisation
ESA TO
  Csaba Jeger
  NAMMO
    Martina Faenza
  ILOT Lukasiewicz
    Zbigniew Gut
Subcontractors
  U. Rome La Sapienza
    Francesco Nasuti
  AVIO
    Attilio Cretella
Empresarios Agrupados Internacional
  CO: Miguel Alcázar
  TO: María Aranda
Prime Contractor

## Slide 7: Project Plan

## Slide 8: Project Deliverables
 | EAI | Urome | AVIO | Nammo | Status
D1: “Propulsion system Models” |  | X | X | X | Delivered and accepted
D2: “Model design document” | X | X |  |  | Delivered pending on final acceptance
D3: “Model Validation Report” |  | X | X | X | Delivered pending on final acceptance
SW1: “ESPSS library extension” | X |  |  |  | Delivered and accepted
SR, ESR, TAS, FR, CCD, FP, SRF | X |  |  |  | Delivered and accepted
KOM= 2021 / 11 / 19
MS1 = KOM + 4 M = 2022 / 03 / 21
MS2= MS1 + 8 M = 2022 / 11 / 24
MS3 = MS2 + 10 M = 2023 / 10 / 16

## Slide 9: Task 1: models identification

## Slide 10: Project Plan

## Slide 11: TASK 1: Models identification
Models identification:
  LA SAPIENZA (UROME) WP2100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    REDUCED ORDER FINITE RATE CHEMISTRY
  LUKASIEWICZ (ILOT) WP2300
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 12: TASK 1: Models identification
Models identification:
  LA SAPIENZA (UROME) WP2100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    REDUCED ORDER FINITE RATE CHEMISTRY
  LUKASIEWICZ (ILOT) WP2300
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 13: TASK 1: Models identification
Coking in cooling channels
Heat supply from the chamber in rocket engines can contribute to a carbon deposit layer at the walls. This deposit affects the heat exchange and can lead to too-high temperatures and cause engine failures
A thermal resistance is computed with a semi-empirical approach dependent on 4 parameters and the Reynolds number:
Afterwards, the convective heat transfer coefficient is computed taking into account this contribution

## Slide 14: TASK 1: Models identification
Implementation phase:
  LA SAPIENZA (UROME) WP2100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    REDUCED ORDER FINITE RATE CHEMISTRY
  LUKASIEWICZ (ILOT) WP2300
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 15: TASK 1: Models identification
Heat and mass transfer in novel injectors
a) Pressure losses computation
The pressure losses at injectors will take into account different geometries and types of injectors:
Different geometries are possible:
- Sharp
- Rounded
- Slanted
- Angled inlet

## Slide 16: TASK 1: Models identification
Heat and mass transfer in novel injectors
b) Heat transfer
An improved thermal network has been created for the combustor components, which take into account an axial distribution of the injector holes and walls:
Several nodes compute dynamically the evolution of the temperatures at the walls, taking into account the conduction among them and the ambient. It is possible to activate convection between the cavities and the walls.

## Slide 17: TASK 1: Models identification
Implementation phase:
  LA SAPIENZA (UROME) WP2100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    REDUCED ORDER FINITE RATE CHEMISTRY
  LUKASIEWICZ (ILOT) WP2300
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 18: TASK 1: Models identification
Turbomachinery transient models
A model in open literature has been found that is fully compatible with ESPSS due to its topology. It is based on a work by a group of ISRO (Indian Space Research Organization).
Such work has been selected to be the starting point for the development of the enhanced pump component in ESPSS.
Combination of fluid nodes (conservation of mass and momentum) + thermal nodes (energy)

## Slide 19: TASK 1: Models identification
Implementation phase:
  LA SAPIENZA (UROME) WP2100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    REDUCED ORDER FINITE RATE CHEMISTRY
  LUKASIEWICZ (ILOT) WP2300
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 20: TASK 1: Models identification
Reduced order finite rate chemistry
4 Arrhenius schemes have been proposed after a detailed literature review. They are generated starting from the C1-C4 kinetic mechanism by Zhukov Z-DKM:
TSR-stoic21, general 21 species scheme including initiation chemistry aspects associated to homogeneous ignition
TSR-stoic12, compact 12 species scheme
TSR-lean14, compact 14 species scheme to be operated under fuel-lean conditions
TSR-rich32, a 32 species scheme to be operated under fuel-rich conditions
All the schemes have been tested and validated in terms of equilibrium temperaeture and composition, counter flow diffusion flames and perfecly stirred reactor calculations.
Comparable or superior performance compared to Zhukov scheme.

## Slide 21: TASK 1: Models identification
Implementation phase:
  LA SAPIENZA (UROME) WP2100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    REDUCED ORDER FINITE RATE CHEMISTRY
  LUKASIEWICZ (ILOT) WP2300
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 22: TASK 1: Models identification
Chemical modelling of HTP
HTP modelled as a Perfect Liquid: it keeps simplicity while fulfils all the termal/fluid requirements
Several new properties files have included inside ESPSS, each of them for a different concentration of HTP: 85, 87.5, 90, 92, 95 and 98 %.
Injectors
Showerhead injector is the most prevalent type in monopropellant thrusters. Uniform injection pattern.
Manifold: modelled as a simple, constant 0D volumen
Injector element: 1D momentum equation that computes dP = f (Cd)
Ullage volume: due to ambiguities on physical phenomena in this region is rejected

## Slide 23: TASK 1: Models identification
Catalyst bed modelling
Liquid and gas phase are mechanically coupled.
Solid and fluid are at different temperatures. Thermal losses due to convection and radiation are included in the energy equation
Mixture is composed by:
  H2O Liquid
  HTP Liquid
  H2O2 Gas
  H2O Gas
  O2 Gas
Properties of the mixture are defined by the concentrations of the liquids (HTP_L, H2O_L) in the flow. They have their own evolution equations
Finite rate chemistry is done by bulk reaction models which can be easily linked to test data.
Ergun equation is used for the pressure drop. It expresses the friction factor as function of the Reynolds number and porosity.

## Slide 24: TASK 1: Models identification
Catalyst bed modelling
HTP Decomposition
H2O2 Decomposition
HTP_L
O2_G
H2O_L
H2O_G
H2O2_G
Boiling

## Slide 25: Task 2: models implementation

## Slide 26: Project Plan

## Slide 27: TASK 2: Models implementation
Implementation phase:
  LA SAPIENZA (UROME) WP3100
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
  EMPRESARIOS AGRUPADOS (EAI) WP3200
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR GREEN PROPELLANTS

## Slide 28: TASK 2: Models implementation
Implementation phase:
  LA SAPIENZA (UROME)
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
  EMPRESARIOS AGRUPADOS (EAI)
    MONOPROPELLANT MODELLING
      INJECTORS
      CATALYTIC BED
      CHEMISTRY MODELS
    FINITE RATE FOR LOX/CH4

## Slide 29: TASK 2: Models implementation
Implementation phase:
  LA SAPIENZA (UROME)
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
  Creation of a new component in ESPSS called "Tube_coking" which has a flag for activating coking phenomena.
  Existing Cooling Jacket component in ESPSS has been upgraded, adding this new coking flag as a construction parameter.

## Slide 30: TASK 2: Models implementation
Pyrolysis and Coking formulation
  Released carbon might interact with the walls
  Acts as an insulation coating which can affect the cooling process
  Fluid-dynamics effects not considered
  Time dependent thermal resistance is introduced:
    4 experimental data

## Slide 31: TASK 2: Models implementation
Implementation phase:
  LA SAPIENZA (UROME)
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
  A new injector component has been created: "InjectorLoss", more accurate.
    Set of possible pressure-loss modes: single jet, mixed jets, swirled, closed swirl, open swirl, bipropellant swirl, gas-swirl and perforated plate.
  Two new topological macro-combustors have been added to ESPSS: "Preburner_Plate" and "ChamberNozzleDynamic_Plate".
    Novel injectors, plus a new heat exchange modelling. It has a detailed thermal network for computing the heat exchanged between the injector plate, the combustor walls and the cavities, as well as their temperatures.

## Slide 32: TASK 2: Models implementation
Injector Head for oxygen/methane rocket engine
  Inlet
    Sharp, Rounded, Slanted or Angled Inlet
  Single Jet Injector
  Mixed Jet Injectors
  Swirled Injectors
    Closed Swirl Injectors
    Open Swirl injectors
    Bipropellant swirl injectors
    Gas-swirl injector
  Perforated plate
    Thick plate
    Thin plate

## Slide 33: TASK 2: Models implementation
Heat Exchange for injectors
  Improved thermal network to simulate CH4/O2 injectors
  Thermal Network of Injectors in ESPSS 3.6
  New Thermal Network

## Slide 34: TASK 2: Models implementation
New components
  New PreBurners and CN components created with new thermal network and injectors
    Option to activate or deactive the convection in the injection elements
      FLAG Inj_cov
  ChamberNozzleDynamic_Plate
  Preburner_Plate

## Slide 35: TASK 2: Models implementation
Implementation phase:
  LA SAPIENZA (UROME)
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
    New component: "Pump_chilldown". It is a topological component that is formed by the main fluid stream, plus a secondary stream in charge of chill down.
    The proper heat exchange with the inclusion of thermal nodes and conduction elements has been taken into account.
    A series of discretized volumes have been included to represent the different parts of the pump (impeller, volute, etc.)

## Slide 36: TASK 2: Models implementation
Development of pump component for transient chill down
  The NPSH Calculation and Conservation Equations are the same of the Pump and Pump gen component
  Cooling of the bearing cavity behind the impeller
    Cooling coming from spilled from the main flow

## Slide 37: TASK 2: Models implementation
Implementation phase:
  LA SAPIENZA (UROME)
    COKING IN CJ
    HEAT AND MASS TRANSFER IN NOVEL INJECTORS
    TURBOMACHINERY TRANSIENT MODELS
  EMPRESARIOS AGRUPADOS (EAI)
    MONOPROPELLANT MODELLING
      Injectors
      Catalytic bed
      Chemistry models
    FINITE RATE FOR LOX/CH4

## Slide 38: TASK 2: Models implementation
Finite Rate Chemistry for LOX/CH4 combustions
  Modification of the Abstract combustor components to select Arrhenius cases
    4 options loaded in Arrh_option
      TSR_Stoich-21
      TSR_Stoich-12
      TSR_Lean-14
      Global
    New chemicals included to the CEA database of ESPSS
      CH3, C2H, C3H3, CH3O
      All the schemes have been tested and validated in terms of equilibrium temperature and composition, counter flow diffusion flames and perfectly stirred reactor calculations. The results showed comparable or superior performance compared to the Zhukov scheme.

## Slide 39: TASK 2: Models implementation
Monopropellant HTP
  Development of specific functions for the calculation of properties of liquid/gas mixture in HTP decomposition
    Calculation of P,T of HTP as a function of u and and
      HTP_Mix_state_vs_ru
    Transport properties f(P,T,)
      HTP_visc_vs_pT or HTP_cond_vs_pT
    Thermodynamic properties f(P,T, )
      HTP_prop_vs_pT
        Density,h,Psat,Tboil,vsound
  Integration of property files into ESPSS
    Including multiple perfect liquid files with varying HTP mass composition
      85, 87.5, 90, 92, 95, 98, 100 (%)

## Slide 40: TASK 2: Models implementation
Monopropellant HTP
  Injector HTP component
    Modified Junction with discharge coefficient calculation
      Cd_Constant
      Cd_Table f(Re)
      Cd_Lichtarowicz empirical correlation f(Re)
    Included multiple orificies, calculates actual throat area
    Embebbed in the “InjectorLoss” component
Injector developments for LOX/CH4 case (URome WP3100) +
Injector developments for HTP case (EAI WP3200)

## Slide 41: TASK 2: Models implementation
Monopropellant HTP
Injector developments for LOX/CH4 case (URome WP3100) +
Injector developments for HTP case (EAI WP3200)

## Slide 42: TASK 2: Models implementation
Monopropellant HTP
  CombustHTP component
    Created component based on abstract formulation
    Formulation
      Mixture of chemical components
      Boiling Options
        HTP_Boil1, HTP_Boil2, HTP_Boil2, HTP_BoilKW
AbsCombustorHTP
CombustHTP
AbsCombustorHTP_NP
AbsCombustorMonoProp_HTP
CombustMonoProp_HTP

## Slide 43: TASK 2: Models implementation – SUMMARY
Additional components
Modified/improved components
Coking
Arrhenius schemes of LOX/CH4
COMB CHAMBERS
TURBO MACHINERY

## Slide 44: Task 3: models validation

## Slide 45: TASK 3: Models validation

## Slide 46: TASK 3: Models validation
Clasification of validation activities
  Pre-validation at component level against open literature/use cases
    URome, Lukasiewicz
  Validation at component level against test data
    AVIO, NAMMO
  Validation at engine level against test data
    AVIO, NAMMO
New examples available:
“test_ch4_tsr12”
“test_ch4_tsr21”
“test_ch4_tsrlean14”
“test_coking”
“test_comb_htp”
“test_comb_htp_nozzle”
“test_injMonoprop”
“test_injector_loss”
“test_pump_chilldown”
“test_preburner_plate”

## Slide 47: TASK 3: Models validation
Validation of PreburnerPlate component
  “test_preburner_plate” in ROCKET_EXAMPLES
    Proposed model enables to represent the heating transient
      Uncertainties in shutdown leads to discrepancies
    Reference: “DeRidder, M. A and Anderson, W.E. Heat flux and pressure profiles in an oxygen/hydrogen multielement rocket combustor, JPP 2010”

## Slide 48: TASK 2: Models implementation
Validation of pump component for transient chill down
  “test_pump_chilldown”:
    Good reliability in reproducing the experimental behaviour
    Reference: J Joseph et al. “Chilldown study of cryogenic turbopump bearing coolant cavity”, ICAME 2015

## Slide 49: TASK 3: Models validation
Coking Validation
  “test_coking” in ROCKETS_EXAMPLES
  Kerosene RP1 experimental data, fitted (JP10)
  Reference: “K. Liang, B. Yang, and Z. Zhang, “Investigation of heat transfer and coking characteristics of hydrocarbon fuels,” Journal of Propulsion and Power, 1998”

## Slide 50: TASK 3: Models validation
LOX/CH4 injectors
  Validation
    test_injector_loss in ROCKET_EXAMPLES for the Close swirled with sharp inlet validation
    Reference: “Ahn et al, Experimental Study on the Discharge Coefficient of Bi-Swirl Coaxial Injectors, Journal of Applied Fluid Mechanics, 2019”

## Slide 51: TASK 3: Models validation
Monopropellant Examples
  Test of Catalytic Bed test_comb_HTP in ROCKET_EXAMPLES
  Test of Monopropellant in test_comb_htp_nozzle in ROCKET_EXAMPLES
  Reference: “Paweł Surmacz PhD Thesis. ILOT. “ Experimental studies decomposition process of 98%hydrogen peroxide in composite catalytic beds in rocket engine injection systems”

## Slide 52: TASK 3: Models validation
Validation of LOX/CH4 injectors
  Validation of pressure losses through injectors with two set of experiments:
    Water cold-flow tests: validation of jet injectors (sharp edge, rounded inlet and slanted inlet) and perforated plate with slanted inlet for different mass flows. Perforated plate model shows better performance, with a 20% deviation (uncertainties of measurements)
    Hot-firing tests: data coming from DM1 M10 engine test. Numerical results show very good agreement (below 10% error) for the steady state.
  Thermal network validation taking into account relevant dimensions of the elements.
    Fluidic temperatures are very well reproduced
    Solid temperatures are not well reproduced (effective thermal conductivity, actual exposed surfaces for the heat exchange, position of thermocouples…)
  Reduced order finite rate chemistry
    Two models were validated and compared to the global mechanism in ESPSS: TSR-Stoich-21 and TSR-Stoic-12.
    Data coming from DM1 M10 hot firing tests.
    Good prediction of chamber pressure at steady state (<10% error) and good prediction of the ignition event.

## Slide 53: TASK 3: Models validation
Validation of Pump chilldown
  Several simulations:
    Chilldown
    Transient phases (start-up, shutdown)
  DATA: turbopumps assemblies from DM1 experimental test campaings DM1-02, DM1-04-02.
  Fluid temperatures and most important wall temperatures follow the experimental behavior
  Some differences in other wall temperatures are observed due to uncertainties in the model layout and the 1D approach of ESPSS.
  A major difference was observed during shutdown due to a residual rotational speed near 0-rpm conditions. This has been changed and the correction will be included in the next ESPS version.
Validation of coking
  Several simulations:
    RP-1 (Kerosene)
    Propane
    Jet-A
  Good reproduction of the results by adjusting the semi-empirical parameters to open literature data

## Slide 54: TASK 3: Models validation
LOX/CH4: AVIO validation of M10 DM1 test campaign
  Variables compared:
    Rotational speed, mass flow, outlet pressure of the oxidizer pump
    Pressure and MR of the combustion chamber
  Results are in line with experimental data both in absolute values at steady state and the transient trends.
  Complete engine assembly with new pump and new combustor reproduces with high accuracy the engine real performance (startup, steady, shutdown)
HTP: Nammo validation of PoC1 and PoC4 test campaign
  Variables compared: pressure, temperature, decomposition evolution and mass flow.
  Simulations done with 87.5% concentration of H2O2
  Different operating points tested
  PoC1: general performance with error <10%. Pressure rise faster than in testing due to several causes (decomposition rate of H2O2, flash boiling, Leidenfrost effect, 3D effects, small cavity downstream of injector plate not included…)
  PoC4: general performance with error <10%. Better results for single firing than pulse firing. Combustion chamber temperature rise happens more rapid than in tests. (Uncertainties in the delay of the pressure signal)

## Slide 55: Conclusions and future work

## Slide 56: Conclusions
LOX/CH4
  New pump component is able to follow the trend of the fluidic nodes, while for the nodal temperature the geometry and layout must be as much as possible similar to the real one to have a representative trend
  Simulations at engine level show a high degree of accuracy for reproducing test data results
  Injectors pressure losses tests show <10% error for the hot firing tests when predicting the mass flow
  The use of finite rate schemes penalizes the runtime performance but is of great advantage for a good prediction of the ignition time.
HTP
  Better performance of the “CombustMonoprop_HTP” component than the assembly of “CombustHTP” + “Nozzle”.
  Error below 10% in the most important variables
  Robust model
  No big runtimes

## Slide 57: Future work
LOX/CH4
  Combustor: compute pressure based on Dt (without relying on the chamber mesh)
  Limitation in new chemical schemes: Missing N2 and He in the list of non-condensable fluids
  Dedicated component with finite rate chemistry only to assess performance in transient phases of small thrusters
HTP
  Improve the way in which the geometry of subsonic and supersonic parts are inputted by the user (avoid inconsistencies)
  Improve robustness when the nozzle type is set as “NonIsentropic”
  Handle N2 as pressurizer gas in the system
  Option to specify different porosities along the length of the catalyst.
  Extend HTP component to any other chemical scheme (e.g. Hydrazine…)
  Merge HTP properties functions with previously existing ones in FLUID PROPERTIES library

## Slide 58: Questions ?

## Slide 59: Thank you!