## Slide 1: ASSESSMENT OF AUTOMOTIVE EEE COMPONENTS SUITABILITY FOR SPACE APPLICATIONS
Final presentation

## Slide 2: tABLE OF CONTENTS
Agenda
1
WP1 - AEC-Q Automotive
Part Selection
2
WP2 – Comp. of automotive and Space Approval Testing
3
WP3 - Tests
4
WP4 - Recommendations
5

## Slide 3: agenda
WP1 - AEC-Q Automotive part Selection (F. García Donday, TAS-E)
WP2 - Comparison of automotive and Space Approval Testing (F. García Donday, TAS-E)
Break
WP3 - Test Campaign (F. Waldron, Tyndall National Institute
WP4 – Conclusions and Recommendations (L. de Pablo, TAS-E)

## Slide 4: Wp1 - AEC-Q Automotive Part Selection
AEC QPL Compile an AEC QPL list based on the state of the art
Space and Military PPL & QPL List of the most demanded devices for Space applications.
AEC PPL for Space Generate an update of the AEC PPL for Space applications
1
2
3

## Slide 5: Wp1 - AEC-Q Automotive Part Selection
AEC QPL Compile an AEC QPL list based on the state of the art
Space and Military PPL & QPL List of the most demanded devices for Space applications.
AEC PPL for Space Generate an update of the AEC PPL for Space applications
1
2
3

## Slide 6: Wp1 - AEC-Q Automotive Part Selection
WHAT IS AEC-Q SYSTEM? MAIN STANDARDS
No yet devices qualified by neither AEC-Q102 (Optoelectronics) nor AEC-Q103 (MEMs) nor AEC-Q104 (MCM) reported by manufacturers or distributors. Only AEC-Q100 (IC’s), AECQ101(Discrete) and AEC-Q200 (Passive):
1
INTEGRATED CIRCUITS
DISCRETE OPTOELECTRONIC SEMICONDUCTORS
PASSIVE COMPONENTS
MULTI CHIP MODULES AND MACRO MODULES
DISCRETE SEMICONDUCTORS
1

## Slide 7: Wp1 - AEC-Q Automotive Part Selection
AEC-Q SYSTEM: AUTOMOTIVE QUALIFICATION
There is not a formal AEC QPL list published anywhere. Each manufacturer qualifies internally plants and devices for automotive applications. As per the information published at manufacturer web sites we distinguish three levels of qualification:
CATEGORY A Components “Classified” by the Manufacturer for Automotive. But without recognized formal qualification as per AEC-Q100; AEC-Q101 or AEC-Q200
CATEGORY B Components Published by the manufacturer as being “Qualified” AEC-Q100, or AEC-Q101 or AEC-Q200
CATEGORY C Components Qualified AEC-Q and for which the manufacturer publishes at the web:
      IATF16949 Certificates of manufacturing plants used for AEC devices.
      To have PPAP reports ready / published / available under request
1
1
Notes: Category A corresponds to: connectors, relays, cable/cable assemblies, Potentiometers, Variable Resistors,
switches, etc... not presently covered by standards AEC-Q100/ AEC-Q101/ AEC-Q200. In this category there are
also many devices being “compliant to” AEC but not formally qualified.
Category B corresponds to devices reported in Data Sheet as being qualified to AEC-Q standard, i.e. variable
resistors, switches, etc... not presently covered by standards AEC-Q100/AEC-Q10/AEC-Q200. In this category
there are also many devices being “compliant to” AEC but not formally qualified.
Category C corresponds with most of big manufacturers and many of small Non US manufacturers.

## Slide 8: Wp1 - AEC-Q Automotive Part Selection
THE AEC QPL LIST (Annex 1 - AEC QPL Compilation Final.xls)
    Compilation of an Almost exhaustive AEC-Q QPL with components published at web as being Qualified AEC-Q100, or AEC-Q101 or AEC-Q200:
    22.9Mb excel file with 212288 items listed from 72 families
    Data source: Big manufacturers and Distributors
    117 manufacturers: with info about published certifications IATF16949 / PPAP available
    The real total number of devices qualified to AEC-Q100, AEC-Q101 or AEC-Q200 is estimated to be close to 600 000
    But all or almost all AEC-QPL series are listed in Annex-1, but not all combinations of size, tolerance, voltage, temperature coefficient, etc...
1

## Slide 9: Wp1 - AEC-Q Automotive Part Selection
THE AEC QPL LIST (Annex 1 - AEC QPL Compilation Final.xls)
1

## Slide 10: Wp1 - AEC-Q Automotive Part Selection
THE AEC QPL LIST (Annex 1 - AEC QPL Compilation Final.xls)
  Some conclusions (1/2):
    Most MCM are listed under AEC-Q100
    Most Sensors (pressure, temperature, accelerometers, gyroscopes, magnetic, proximity, hall effect..) are under AEC-Q100, other under AEC-Q200
    More than 70% of the microcircuits meet the Military Temperature Range (grade-0 plus grade-1). Similar for discrete and passive.
    Some passives are rated at very high temperature (resistors, capacitors, current sensor up to 200ºC to 275ºC)
    Packages: some dice. 78% in plastic package. But 20% are encapsulated in ceramic packages like LCC, or mounted in ceramic support (ceramic chip RCL, thermistors, filters, diodes). Less than 1% is found in metal packages.
    Majority are non hermetic non cavity. Some hermetic by technology (Crystal, oscillators and MEM, SAW Filters). Some new RF/MW devices work better inside air cavity package, these “almost” hermetic adhesive sealed ceramic lid.
    Critical packages (BGA, QFN, DFN, CSP), recognized by the automotive community as assembly critical because more sensitive to thermal fatigue with power on/off thermal cycling represents around 14% of AEC-Q100 microcircuits. DFN/QFN very popular in RF/MW, BGA/LGA almost “omnipresent” for high count FPGA/DSP/uControllers.
    SMD versus Through Hole. SMD accounts for 97%, while 3% for DIP axial, etc…
    Standard Chip Sizes: 0402, 0603, 0805, 1206, 1210, extended from capacitor and resistors to inductors, thermistors, EMI filters, diodes (DFN-2). Same trend seems to be extended to transistors (DFN-3) and MEM oscillators (DFN-4).
1

## Slide 11: Wp1 - AEC-Q Automotive Part Selection
THE AEC QPL LIST (Annex 1 - AEC QPL Compilation Final.xls)
  Some conclusions (2/2):
    Most (97%) but not all are published as RoHs compliant. But some with exception for high temperature solders
    Most manufacturers are from US & Europe & Japan, but with manufacturing plants certified for automotive as per IATF16949 in Far East: mainly China and Taiwan.
    Some European are very active as EPCOS/TDK, Fastron, Infineon Technologies, Jauch Quartz, RF360 (Qualcomm/TDK), ROHM Semiconductor, TDK-Micronas, Vishay / BC Components, Vishay / Beyschlag, Wurth Electronics (in Germany). ATMEL Microchip Technology; ST Microelectronics (in France). Melexis Technologies NV (in Belgium). IQD Frequency Products; Knowles / Syfer; TT Electronics; Welwyn Components / TT Electronics (in UK). Nexperia & NXP in Netherlands. Nordic Semiconductor in Norway. Micro Crystal in Switzerland.
    Top-10 IC suppliers accumulate 85% of automotive, and Top-19 around 95% for more than 70 suppliers
    Some technologies almost not seen in Space: Power GaN; Power SiC; MEM (oscillators); Sensors: pressure, temperature, accelerometers, gyroscopes, ARM magnetic, proximity, hall effect, ambient light, angle and linear position, measuring Infrared Emitters; High End Memories (DDR, Flash, FRAM, MRAM), microprocessors and FPGAs; Very Low Voltage Logic Families (17SZ; 27WZ; 37WZ; 74ABT; 74AUP; 74AVC; 74AXC; LSF; TCB; TWL; TXB; TXS, etc..); Triacs, Thyristor, SCRs; Aluminium Capacitors; Safety capacitors (line to ground capacitors); Ceramic Disc capacitors; BAW Filters; Varistors; Resettable fuses; Battery chargers, battery management; USB protection, Lighting Protection Diodes; Transponder coils, etc.
    Some technologies forbidden for Space: Aluminium Electrolytic Capacitors; Non swept Quartz and Quartz-based Oscillators; fuses: Resettable PPTC & wire link; SCR / Thyristor; Varistors, etc.
1

## Slide 12: Wp1 - AEC-Q Automotive Part Selection
AEC QPL Compile an AEC QPL list based on the state of the art
Space and Military PPL & QPL List of the most demanded devices for Space applications.
AEC PPL for Space Generate an update of the AEC PPL for Space applications
1
2
3

## Slide 13: Wp1 - AEC-Q Automotive Part Selection
COMPILE A LIST OF THE MOST DEMANDED DEVICES FOR SPACE APPLICATIONS (Annex 2 & 3):
Create a list of the most used devices in space, based on the following standards and experience from TAS:
  Sources: ESCC PPL; ESCC QPL; ESCC QML; ESCC HCPL; NPSL; GSFC QPL; JAXA QPL
  Other sources : TAS, AIRBUS, Projects, Constellations,
  Most popular MIL QPL/QML for Space
  Final result:
    Annex 2 - Space PPL.xls
    Annex 3 - MIL QML QPL NASA.xlsx

## Slide 14: Wp1 - AEC-Q Automotive Part Selection
AEC QPL Compile an AEC QPL list based on the state of the art
Space and Military PPL & QPL List of the most demanded devices for Space applications.
AEC PPL for Space Generate an update of the AEC PPL for Space applications
1
2
3

## Slide 15: Wp1 - AEC-Q Automotive Part Selection
COMPILE AN AEC-Q SPACE PPL USING (1/2):
  List of AEC-Q Preferred manufactures for Space (criteria: big manufacturers with a diversified portfolio of AEC-QPL devices and series; with plants dedicated to AEC full certified as per IATF16949 and with PPAP ready to be provided to Space Customers when requested, with previous heritage in launchers (Vega, Ariane-6), and/or new Space Constellations, without bad results in qualification data (constructional analysis, incoming, etc.), European preferred, etc.)
  Preferred families of AEC-Q devices for Space (families demanded for Space, excluding forbidden families, etc.)
  Extended Temperature range -55ºC to +100ºC minimum.
  Preferred packages (exclude through hole, critical BGA/QFN/DFN…)
  Mature but not obsolescent devices (exclude not recommended for new designs)
  For Series (passive, diodes, etc..), list only one representative item of the series.

## Slide 16: Wp1 - AEC-Q Automotive Part Selection
COMPILE AN AEC-Q SPACE PPL USING (2/2):
  Exclude those technologies known to be very likely sensitive to heavy ion induced destructive effects (SEL/SEB/SEGR), by generic literature or previous radiation tests.
  Use also Preliminary ESA AEC PPL
  Exclude, specifically for Space PPL Part-1, those devices/manufacturers with ITAR or EAR ECCN export control restrictions.
  Exclude, specifically for Space PPL Part-1, those devices/series for which interest for Space is reduced due to Unit price is not less than 1/10th of the one of Space Equivalent device, or performances are equal to the ones of the space equivalent device. Focused on those devices interesting in Space because much lower units prices, much better electrical performances as compared to Space available equivalent devices, nothing similar available in hirel
  Preference to parts from Manufacturers with an active system of reporting PCN/PDNs
  Preference to European Parts

## Slide 17: Wp1 - AEC-Q Automotive Part Selection
AND ALSO, MANUFACTURERS PREFERRED FROM SPACE SHOULD BE:
  Those big manufacturers with a diversified portfolio of AEC-QPL devices and series
  With manufacturer plants dedicated to AEC full certified as per IATF16949 and with PPAP ready to be provided to Space Customers when requested
  With previous heritage in launchers (Vega, Ariane-6), and/or new Space Constellations
  Without bad results in qualification data (constructional analysis, incoming, Fischerscope, etc...)
  European preferred.

## Slide 18: Wp1 - AEC-Q Automotive Part Selection
NEW AEC-Q SPACE PPL:
Comparing lists in Annex-1 and in Annex-2+Annex-3 we see what is summarised Annex - 4 . Showing what families of devices are used in Space versus what families are qualified automotive AEC-Q.

## Slide 19: Wp1 - AEC-Q Automotive Part Selection
NEW AEC-Q SPACE PPL:
Comparing lists in Annex-1 and in Annex-2+Annex-3 we see what is summarised Annex - 4 . Showing what families of devices are used in Space versus what families are qualified automotive AEC-Q.
AN-1 AEC QPL
AN-2&3
Space PPL
Annex 4
AEC-Q Space PPL

## Slide 20: Wp1 - AEC-Q Automotive Part Selection
SELECTED AEC-Q CANDIDATES FOR TESTING
  General Requirements:
    High production volumen
    European manufacturers
    Variety of families
Part Number | Description | Manufacturer
TS974IYPT | Output rail-to-rail very low-noise operational amplifier | ST Microelectronics
SMBD914E6327HTSA1 | Silicon Switching Diode, high speed | Infineon
12105C475K4Z | Capacitors fixed chips ceramic Dielectric type II flexible termination based on type 1210 | AVX LTD
Notes: Añadir por

## Slide 21: WP2 - Comparison of automotive and Space Approval Testing
General Comparison Space versus Automotive Mission requirements
General Policy Comparison between AEC-Q, QML/QPL, ECSS-Q-ST-60-13C, Enhanced Plastic Microcircuits
General listing of test methods and procedures (Para. 1) for AEC, MIL, ESCC, ECSS-QST-60-14, NASA GSFC PEMS-INT-001, JEDEC (JESD22 series and other relevant test methods), IEC, etc...
Some feedback and impressions got from AEC conferences and workshop, as well as from interviews and contacts with AEC manufacturers (Para. 10).
Summary of results and conclusion from this comparative (Para. 11).
Proposal of testing for the three candidates (Para. 12).

## Slide 22: WP2 - Comparison of automotive and Space Approval Testing
Detailed Test Methods Comparison for:
  Microcircuits and Hybrids: AEC-Q100 vs ECSS-Q-ST-60-13C vs ESCC 9000 / ESCC 9010 / ESCC 9020 / ECSS-Q-ST-60-05C1 vs MIL-PRF-38535 / MIL-PRF-38534 / MIL-STD-883 TM5004/TM5005 vs NASA GSFC PEM-INST-001 / NASA GSFC INST-EEE-002 (sections M2-M3-M4)
  Semiconductors: AEC-Q101 vs ECSS-Q-ST-60-13C vs ESCC 5000 / ESCC 5010 vs MIL-PRF-19500
  Passive: AEC-Q200 vs ESCC 3001 to ESCC 3012 / ESCC 3501 / ESCC 4001 to ESCC 4009 / ESCC 3201 vs MIL-PRF-55681; MIL-PRF-55365; MIL-PRF-83421; MIL-PRF-83401; MIL-PRF-55342; MIL-PRF-23648; MIL-PRF-14409; MIL-PRF-27; MIL-PRF-21038; MIL-PRF-3098; MIL-PRF-28861
  Optos & LEDS: AEC-Q102 vs ECSS-Q-ST-60-13C vs ESCC 5000 / ESCC 5010 vs MIL-PRF-19500
  MEMs & Sensors: AEC-Q103 / AEC-Q200 vs ECSS-Q-ST-60-13C vs ESCC 9000 / ESCC 9010 / ESCC 9020 / ECSS-Q-ST-60-05C1 vs MIL-PRF-38535 / MIL-PRF-38534 / MIL-STD-883 TM5004/TM5005 vs NASA GSFC PEM-INST-001 / NASA GSFC INST-EEE-002 (sections M2-M3-M4)
  Multichip Module (MCM): AEC-Q103 / AEC-Q200 vs ECSS-Q-ST-60-13C vs ESCC 9000 / ESCC 9010 / ESCC 9020 / ECSS-Q-ST-60-05C1 vs MIL-PRF-38535 / MIL-PRF-38534 / MIL-STD-883 TM5004/TM5005 vs NASA GSFC PEM-INST-001 / NASA GSFC INST-EEE-002 (sections M2-M3-M4)

## Slide 23: WP2 - Comparison of automotive and Space Approval Testing
Detailed Testing Flows Comparison for
  Microcircuits: AEC-Q100 vs ECSS-Q-ST-60-13C vs NASA GSFC PEM-INST-001
  Semiconductors: AEC-Q101 vs ECSS-Q-ST-60-13C vs NASA GSFC PEM-INST-001
  Passive. Ceramic Chip Resistors: AEC-Q200 vs QCI A-B-C from MIL-PRF-55342
  Passive. Solid Tantalum Chip Capacitors: AEC-Q200 vs QCI A-B-C from MIL-PRF-55365
  Passive. Ceramic Chip Capacitors: AEC-Q200 vs QCI A-B-C from MIL-PRF-55681
  Passive. Magnetic Devices: AEC-Q200 vs QCI A-B-C from MIL-PRF-83446 & MIL-STD-981C1

## Slide 24: WP2 - Comparison of automotive and Space Approval Testing
Listing of Methods and Procedures used for Comparison
  AEC-Q ancillary documents (38)
  MIL-STD-883L Test Methods (108) + MIL-STD-750 (206) + MIL-STD-202 (41)
  ESCC Basic Specifications (196)
  EIA/JEDEC JESD22 series (44)
  Other relevant EIA/JEDEC documents JEP, JESD, J-STD (102)
  IEC relevant tests (46)
  ECSS-Q-ST-60-13C tests (evaluation, screening, lot acceptance, constructional analysis, DPA)
  NASA GSFC PEM-INST-001 testing (qualification, screening, DPA)

## Slide 25: WP2 - Comparison of automotive and Space Approval Testing
Accede Workshop In Seville Nov’2019 and ESCCON March’2021

## Slide 26: WP2 - Comparison of automotive and Space Approval Testing
Results and Conclusions from Comparison
  Generally stronger Qualification for AEC-Q than for Space and exigence trend in automotive is increased for automatic driving.
  An exception is Radiation (TID, TNID, SEE) of course!!. Also vibration and shock for cavity devices qualified in automotive for typical transport loads, and Space could be higher. Also non hermetic cavity need to be qualified for vacuum (corona & multination for RF)
  Large diversity of available components excepting RF, hybrids and High Voltage, what is changing more and more
  Not the same strategy for microcircuits than discrete or passive. Cpk and ppm estimation
  Lack of screening in AEC justified by a zero failures (ppb failure rate cpK>2.0) strategy
  Process change control needed
  Very old qualification data in many cases (>10 years sometimes) justified by no changes, SPC control, and AEC-Q qualification on devices using same package and assembly techniques, and from the same die technological family
  Support from Manufacturers could be difficult