## Slide 1
DESI CC
4th June 2024

## Slide 2: AGENDA
Introduction of project
Study Phase
EGS CC Integration
Conclusion

## Slide 3: Introduction Project. EGSE Common Core (EGS-CC)
What is EGS-CC?
A new software framework developed for Spacecraft, AIT and Operations.
Development Status:
Development completed, entering maintenance phase
Collaborative effort led by ESA
Primary Aim:
To create a standardized platform for Central Checkout Systems for AIT and Operational Mission Control Systems.

## Slide 4: Introduction Project. Rovsing EGSE Controller Features
EGSE Management:
Manages Hardware Units: Efficient management of various subsystems.
Subsystem Examples: Umbilical Power, Battery Simulators, Solar Array Simulators,
Integrated Software Components:
Man-Machine Interface (MMI)
CCS Interface
Logger and Archive Modules
Business Logic
Hardware Adaptors
Script Engine
Reporting Module

## Slide 5: Introduction Project. Project Plan Overview

## Slide 6: Introduction Project. Timeline Overview
03/2017
KO
10/2017
Study Phase
Design Phase
01/2020
06/2023
Close out
Design, Develop and Test Phase
06/2024

## Slide 7: Study Phase. Initial High-Level DESI-CC Goals
The initial high-level goals of DESI-CC were to integrate the Rovsing EGSE Controller software core to the EGS-CC software framework. Examples of potential application:
• Adaptation to EGS-CC native software interfaces
• Compatibility to EGS-CC Common Data model
• Harmonization of MMI look and feel
• Overall technology harmonization

## Slide 8: Study Phase Results
Setup seen from Common core
First initial idea following with EGSE-CC:
Define “EGS-CC Conceptual Data Model” in XTCE
  Define TM/TC packets. Rovsing FEE Controller should be able to import these definitions for internal usage.
  Create Displays.
  Create Procedures/Scripts for Testing.
Connect to Rovsing FEE Controller via the M&C Adaption component using EDEN/PUS protocol.
Use EGS-CC for logging/archiving.
Use EGS-CC for User Interface

## Slide 9: EGS CC Integration Diagram Overview

## Slide 10: EGS CC Integration Key Features Achieved
1. Import TM/TC in EGS-CC: EGS-CC knows generic telecommands from the Rovsing Controller SW.
2. Connect to Rovsing FEE Controller via the M&C Adapters: The EGS-CC test environment is sending telecommands and receiving telemetry from the Rovsing Controller SW.
3. Create Procedures/Scripts for Testing: The EGS-CC can run test scripts reading telemetry from the Rovsing Controller SW and sending telecommands to it
4. Use EGS-CC for logging/archiving The EGS-CC takes care of logging and archiving of all TM/TCs.
5. Utilize EGS-CC UDD for displays: Use EGS-CC as a CCS to control the Rovsing Controller SW as a SCOE system. UDD displays represent SCOE Controller. Output is a set of UDD that is linked to the SCOE Controller TDM

## Slide 11: EGS CC Integration overall EGSCC UI
“Live” TM/TC in communication with the SCOE controller.

## Slide 12: EGS CC Integration MMI Features
Rovsing Native MMI
EGSCC UDD
UMB SCOE SYSTEM

## Slide 13: EGS CC Integration MMI Features Main Power Supply
Control
Control
Status
Status

## Slide 14: EGS CC Integration MMI Battery Charger
Control
Control
Status
Status

## Slide 15: EGS CC Integration MMI Umbilical Subsystem
Control
Control
Status
Status

## Slide 16: EGS CC Integration MMI System Status
Status
Status
Status
Status

## Slide 17: EGS CC Integration Key Features Achieved
  MME Model
  Telemetries
  Telecommands
  Mission Model

## Slide 18: EGS CC Integration MiB import
Key Points:
Adding arguments to the telecomands manually
Structure the housekeeping package correctly with parameters
Generate specific arguments and parameters
Unique IDs must be take into consideration when you generate new items

## Slide 19: EGS CC Integration Acceptance Test setup/configuration
Rovsing Controller Software
  Setup C&C protocol or EDEN protocol.
DESI CC Software
  EGSCC-Rovsing on Linux (Ubuntu)
Docker Setup
  Linux PC (Ubuntu)
Mission Model Editor (MME)
  Install Temurin 11

## Slide 20: Conclusion and Future Work
Project Goal:
  To create an initial framework for the EGS-CC and Rovsing EGSE Controller.
Potential Benefits:
  Standardization of AIT and operations.
  Enhanced efficiency and reliability.
  Improved interoperability across the industry.
Industry Impact:
  Streamlined processes.
  Greater consistency in spacecraft testing and operations.
Lessons learned:
UDD editor is very time consuming
MME need to be improve
Complex system -> Clear and detail Documentation
Easier to upload TDM in the EGS-CC and clone items
Custom tools
Simplify/streamline MIB -> TDM conversion, benefit magnified as this will be a recurring task

## Slide 21
ANY QUESTIONS OR COMMENTS?